## Slide 1
START HERE
Your Verilog → a checked chip layout
SHIFT REGISTER QUICKSTART • Guide page 1
Open reference ↗
1
Bring your working Verilog design. Leave with a tested Tiny Tapeout layout.
Your Verilog
existing design
Connect pins
Tiny Tapeout wrapper
Test
check the behaviour
Build layout
GDS + checks
Save evidence
ready for review
Recommended learning order • test, docs and gds workflows start independently.
01
Open the HTML guide and the starter ZIP beside GitHub.
02
Follow guide pages 2–12. Tick each checkpoint before continuing.
CHECK
I have opened the guide, signed in to GitHub and found the starter ZIP.
Notes: Guide page 1: Your Verilog → a checked chip layout
You already have a working Verilog design. This guide shows how to put it inside Tiny Tapeout, test the connections and build its layout. We use an eight-bit shift register throughout.
Keep this guide beside your browser. Use the interactive HTML version for the clock experiment and tick each checkpoint as you finish.
Sign in to a free GitHub account. Download shift-register-starter.zip and extract it: on Windows, right-click → Extract All. Open the extracted folder containing info.yaml, src, test and docs. GitHub stores your project and runs the tools.
Follow pages 2–12 in order. Page 13 is your final checklist and help sheet. You need no chip board or local tool installation for this browser route.
Tiny Tapeout = A service that combines small circuit designs on a shared chip. Its template includes the build tools.
Layout = The shapes and wires used to manufacture the circuit. GDS is the file format that stores them.
Check: I have opened the guide, signed in to GitHub and found the starter ZIP.
Open GitHub / create a free account: https://github.com/signup

## Slide 2
KEEP YOUR CIRCUIT
1. Start with the design you already have
SHIFT REGISTER QUICKSTART • Guide page 2
2
Eight stored bits. One input bit. One clock edge at a time.
01
Extract the starter ZIP. Open src/shift_register.v.
02
Reset clears; enable shifts; otherwise hold.
03
Shift 1, 0, 1 in the HTML clock experiment.
src/shift_register.v
always @(posedge clk) begin
if (rst)
q <= 8'b00000000;
else if (enable)
q <= {q[6:0], serial_in};
end
endmodule
Excerpt • full file in the guide and example download
CHECK
I know my circuit’s reset polarity, shift direction and enable behaviour.
Notes: Guide page 2: 1. Start with the design you already have
Our starting file is shift_register.v. It stores eight bits. Each rising clock edge moves the bits one position towards bit 7 and puts serial_in into bit 0, when enable is 1.
In the extracted folder, open src/shift_register.v with a text editor such as Notepad or VS Code. This is the reusable circuit; it does not contain Tiny Tapeout pin names.
Read its rule: reset wins; otherwise enable shifts; otherwise the stored value stays the same. Reset is synchronous: it takes effect at a rising clock edge.
Try the clock experiment in the HTML guide. From reset, shift in 1, then 0, then 1. Predict the eight-bit output after each edge.
RTL = The Verilog description of the circuit’s behaviour and registers.
Pause and predict: Starting at 00000000, what do inputs 1, 0, 1 produce after three enabled edges?
Answer: 00000001 → 00000010 → 00000101. A disabled edge keeps 00000101.
Check: I know my circuit’s reset polarity, shift direction and enable behaviour.
Full code (src/shift_register.v):
`default_nettype none
// Existing design: 8-bit serial-in, parallel-out shift register.
module shift_register (
input wire clk,
input wire rst, // 1 clears q on the next rising clock edge
input wire enable, // 1 shifts; 0 holds the stored value
input wire serial_in, // new bit enters q[0]
output reg [7:0] q
);
always @(posedge clk) begin
if (rst)
q <= 8'b00000000;
else if (enable)
q <= {q[6:0], serial_in};
end
endmodule

## Slide 3
KEEP YOUR CIRCUIT / DETAIL
1. Start with the design you already have — in practice
SHIFT REGISTER QUICKSTART • Guide page 2
3
PAUSE & PREDICT
Starting at 00000000, what do inputs 1, 0, 1 produce after three enabled edges?
Answer: 00000001 → 00000010 → 00000101. A disabled edge keeps 00000101.
CHECK
I know my circuit’s reset polarity, shift direction and enable behaviour.
Notes: Guide page 2: 1. Start with the design you already have
Our starting file is shift_register.v. It stores eight bits. Each rising clock edge moves the bits one position towards bit 7 and puts serial_in into bit 0, when enable is 1.
In the extracted folder, open src/shift_register.v with a text editor such as Notepad or VS Code. This is the reusable circuit; it does not contain Tiny Tapeout pin names.
Read its rule: reset wins; otherwise enable shifts; otherwise the stored value stays the same. Reset is synchronous: it takes effect at a rising clock edge.
Try the clock experiment in the HTML guide. From reset, shift in 1, then 0, then 1. Predict the eight-bit output after each edge.
RTL = The Verilog description of the circuit’s behaviour and registers.
Pause and predict: Starting at 00000000, what do inputs 1, 0, 1 produce after three enabled edges?
Answer: 00000001 → 00000010 → 00000101. A disabled edge keeps 00000101.
Check: I know my circuit’s reset polarity, shift direction and enable behaviour.
Full code (src/shift_register.v):
`default_nettype none
// Existing design: 8-bit serial-in, parallel-out shift register.
module shift_register (
input wire clk,
input wire rst, // 1 clears q on the next rising clock edge
input wire enable, // 1 shifts; 0 holds the stored value
input wire serial_in, // new bit enters q[0]
output reg [7:0] q
);
always @(posedge clk) begin
if (rst)
q <= 8'b00000000;
else if (enable)
q <= {q[6:0], serial_in};
end
endmodule

## Slide 4
BROWSER • GITHUB
2. Make your own Tiny Tapeout project
SHIFT REGISTER QUICKSTART • Guide page 3
Open reference ↗
4
Make your own copy of the official SKY Verilog template.
01
Open TinyTapeout/ttsky-verilog-template.
02
Use this template → Create a new repository.
03
Choose your account. Name: tt-shift-register. Visibility: Public.
GitHub’s official screenshot shows the template menu. Use this control on the SKY template page.
CHECK
My repository belongs to my account and contains src, test, docs and info.yaml.
Notes: Guide page 3: 2. Make your own Tiny Tapeout project
A template is a ready-made set of folders and automation. A repository is your own saved project on GitHub.
Open the official HDL templates page below. Choose the SKY Verilog template used in this lesson. Confirm the repository is TinyTapeout/ttsky-verilog-template.
Sign in. Select Use this template → Create a new repository. Choose your own account as Owner.
Name it tt-shift-register, choose Public, and create it. Check that the new page begins with YOUR username. All later edits happen in this new repository.
Check: My repository belongs to my account and contains src, test, docs and info.yaml.
Official Tiny Tapeout templates: https://tinytapeout.com/hdl/templates/
SKY Verilog template: https://github.com/TinyTapeout/ttsky-verilog-template

## Slide 5
BROWSER • SETTINGS
3. Turn on the build and results page
SHIFT REGISTER QUICKSTART • Guide page 4
Open reference ↗
5
Actions runs your tools. Pages shows the layout.
01
Open Actions. Enable workflows if asked.
02
Settings → Pages → Source: GitHub Actions.
03
Keep .github, src/config.json and test/requirements.txt.
Enlarged detail. Official Tiny Tapeout FAQ image: Source is set to GitHub Actions. Its example repository name may differ from yours.
CHECK
Actions is available and Pages → Source says GitHub Actions.
Notes: Guide page 4: 3. Turn on the build and results page
GitHub Actions runs the checks for you. GitHub Pages displays the finished layout in a browser.
In your new repository, open Actions. If you see an enable-workflows banner, enable it; otherwise continue.
Open Settings → Pages. Under Build and deployment, change Source to GitHub Actions.
Return to Code. Keep the template’s .github folder, src/config.json and test/requirements.txt. The starter changes your design files, while these files supply the tools.
Workflow = A saved recipe of jobs that GitHub runs, such as test or gds.
Check: Actions is available and Pages → Source says GitHub Actions.
Pages troubleshooting: https://tinytapeout.com/faq/#my-github-action-is-failing-on-the-pages-part

## Slide 6
THE IMPORTANT ADAPTATION
4. Plan how your signals reach the chip pins
SHIFT REGISTER QUICKSTART • Guide page 5
6
A wrapper connects your signal names to Tiny Tapeout’s fixed ports.
01
ui_in[0] → serial input. ui_in[1] → shift enable.
02
Clock connects directly. Invert rst_n to make the core reset.
03
q → uo_out. Set unused uio_out and uio_oe to zero.
ui_in[0] serial input
ui_in[1] enable
clk clock
rst_n active-low reset
~
Your shift
register
uo_out
8 bits
CHECK
I can trace every used chip pin to a signal in my existing design.
Notes: Guide page 5: 4. Plan how your signals reach the chip pins
Your circuit has its own signal names. Tiny Tapeout expects a fixed set of ports. A wrapper is a small Verilog module that connects the two.
Use ui_in[0] for serial_in and ui_in[1] for the circuit’s enable. Bits 2–7 are unused.
Connect clk directly. The platform’s rst_n is active low: 0 requests reset. Our circuit’s rst is active high, so connect rst to ~rst_n.
Send all eight q bits to uo_out. We do not use the bidirectional pins: set uio_out and uio_oe to zero. Keep all required wrapper ports.
Port = A named input or output of a Verilog module.
Active low = The function is requested with 0 rather than 1.
Pause and predict: Is ena the same signal as our shift enable?
Answer: No. ena selects this project on the shared chip. Our shift enable is ui_in[1]. This core uses only ui_in[1] to decide whether to shift.
Check: I can trace every used chip pin to a signal in my existing design.

## Slide 7
THE IMPORTANT ADAPTATION / DETAIL
4. Plan how your signals reach the chip pins
SHIFT REGISTER QUICKSTART • Guide page 5
7
PAUSE & PREDICT
Is ena the same signal as our shift enable?
Answer: No. ena selects this project on the shared chip. Our shift enable is ui_in[1]. This core uses only ui_in[1] to decide whether to shift.
CHECK
I can trace every used chip pin to a signal in my existing design.
Notes: Guide page 5: 4. Plan how your signals reach the chip pins
Your circuit has its own signal names. Tiny Tapeout expects a fixed set of ports. A wrapper is a small Verilog module that connects the two.
Use ui_in[0] for serial_in and ui_in[1] for the circuit’s enable. Bits 2–7 are unused.
Connect clk directly. The platform’s rst_n is active low: 0 requests reset. Our circuit’s rst is active high, so connect rst to ~rst_n.
Send all eight q bits to uo_out. We do not use the bidirectional pins: set uio_out and uio_oe to zero. Keep all required wrapper ports.
Port = A named input or output of a Verilog module.
Active low = The function is requested with 0 rather than 1.
Pause and predict: Is ena the same signal as our shift enable?
Answer: No. ena selects this project on the shared chip. Our shift enable is ui_in[1]. This core uses only ui_in[1] to decide whether to shift.
Check: I can trace every used chip pin to a signal in my existing design.

## Slide 8
EDIT • src/project.v
5. Add the wrapper around your design
SHIFT REGISTER QUICKSTART • Guide page 6
Open reference ↗
8
Keep the existing circuit. Add one small module around it.
01
Replace src/project.v with the supplied wrapper.
02
Keep tt_um_student_shift_register for this exercise.
03
The instance below joins each circuit port to its chip signal.
src/project.v
shift_register core (
.clk (clk),
.rst (~rst_n),
.enable (ui_in[1]),
.serial_in (ui_in[0]),
.q (uo_out)
);
Excerpt • full file in the guide and example download
CHECK
My wrapper has the eight required ports and instantiates shift_register with the intended connections.
Notes: Guide page 6: 5. Add the wrapper around your design
Open the supplied project.v. It creates one instance of your shift register and connects the signals from page 5. The shift-register code itself stays reusable.
Use the complete supplied project.v as the replacement for the template’s example.
For this first run, keep tt_um_student_shift_register unchanged everywhere. For a later submission, choose your own unique name beginning tt_um_ and change all three locations on page 7.
Notice that ~ means invert: ~rst_n converts the reset convention. uio_oe = 0 makes every bidirectional pin an input.
Check: My wrapper has the eight required ports and instantiates shift_register with the intended connections.
Tiny Tapeout interface rules: https://tinytapeout.com/hdl/important/
Full code (src/project.v):
`default_nettype none
// Wrapper: connects the existing design to Tiny Tapeout's fixed ports.
module tt_um_student_shift_register (
input wire [7:0] ui_in,
output wire [7:0] uo_out,
input wire [7:0] uio_in,
output wire [7:0] uio_out,
output wire [7:0] uio_oe,
input wire ena,
input wire clk,
input wire rst_n
);
shift_register core (
.clk (clk),
.rst (~rst_n), // Tiny Tapeout reset is low; core reset is high
.enable (ui_in[1]),
.serial_in (ui_in[0]),
.q (uo_out)
);
// Bidirectional pins are unused. A 0 in uio_oe means input direction.
assign uio_out = 8'b00000000;
assign uio_oe = 8'b00000000;
// ena is Tiny Tapeout's project-selection signal, not shift enable.
wire _unused = &{ena, ui_in[7:2], uio_in, 1'b0};
endmodule

## Slide 9
EDIT • THREE NAMES, TWO LISTS
6. Tell both tools which files to use
SHIFT REGISTER QUICKSTART • Guide page 7
9
Both tools need both files. Three top-module names must agree.
src/project.v
module name
info.yaml
top_module
test/tb.v
instance name
Both source lists: project.v + shift_register.v
01
One top name: tt_um_student_shift_register.
02
Two source lists: project.v and shift_register.v.
CHECK
All three top-module names match; both source lists contain both Verilog files.
Notes: Guide page 7: 6. Tell both tools which files to use
The layout builder and simulator read separate source lists. Both must find your core and wrapper. The top module is the outermost circuit the tools should build.
In info.yaml, under project, use top_module: "tt_um_student_shift_register" and source_files: ["project.v", "shift_register.v"]. These filenames refer to files inside src.
In test/Makefile, set PROJECT_SOURCES = project.v shift_register.v. Use the supplied complete Makefile so the surrounding test setup remains intact.
In test/tb.v, the module instantiated as user_project must be tt_um_student_shift_register. The supplied tb.v already does this.
Testbench = Simulation-only code that connects the design to its test. It is not manufactured.
Check: All three top-module names match; both source lists contain both Verilog files.

## Slide 10
EDIT • THREE NAMES, TWO LISTS / DETAIL
6. Tell both tools which files to use — in practice
SHIFT REGISTER QUICKSTART • Guide page 7
10
Location | Must agree
src/project.v | module tt_um_student_shift_register
info.yaml | top_module: tt_um_student_shift_register
test/tb.v | tt_um_student_shift_register user_project
info.yaml source_files | project.v + shift_register.v
test/Makefile PROJECT_SOURCES | project.v + shift_register.v
CHECK
All three top-module names match; both source lists contain both Verilog files.
Notes: Guide page 7: 6. Tell both tools which files to use
The layout builder and simulator read separate source lists. Both must find your core and wrapper. The top module is the outermost circuit the tools should build.
In info.yaml, under project, use top_module: "tt_um_student_shift_register" and source_files: ["project.v", "shift_register.v"]. These filenames refer to files inside src.
In test/Makefile, set PROJECT_SOURCES = project.v shift_register.v. Use the supplied complete Makefile so the surrounding test setup remains intact.
In test/tb.v, the module instantiated as user_project must be tt_um_student_shift_register. The supplied tb.v already does this.
Testbench = Simulation-only code that connects the design to its test. It is not manufactured.
Check: All three top-module names match; both source lists contain both Verilog files.

## Slide 11
EDIT • info.yaml AND docs/info.md
7. Describe the design and its clock
SHIFT REGISTER QUICKSTART • Guide page 8
11
Describe how to use the circuit. Keep its clock settings consistent.
01
info.yaml: your author name, title and correct pin labels.
02
docs/info.md: behaviour, test procedure and hardware needs.
03
50 MHz target = 20 ns per clock cycle.
Place | Clock setting
info.yaml | clock_hz: 50000000
src/config.json (template) | CLOCK_PERIOD: 20 (nanoseconds)
test/test.py cycle() | 10 ns low + 5 ns to sample + 5 ns = 20 ns
CHECK
My descriptions, pin map and clock settings agree with the actual design.
Notes: Guide page 8: 7. Describe the design and its clock
The metadata identifies your project. The datasheet explains how someone can use its pins.
Open the supplied info.yaml. Replace the example author with your name. Keep meaningful title and description text, language Verilog, and the pin labels that match page 5. Keep every required pin key.
Open docs/info.md. Check its How it works, How to test and External hardware sections. It should say: reset clears on an edge; ui_in[1] enables shifting; ui_in[0] supplies the next bit.
For the first exercise keep the supplied 50 MHz target and the current SKY configuration’s 20 ns clock period. The Python test uses 20 ns too. Metadata alone does not change the physical timing constraint.
Metadata = Settings and descriptions about your project.
50 MHz / 20 ns = 50 million clock cycles each second; one cycle lasts 20 nanoseconds.
Check: My descriptions, pin map and clock settings agree with the actual design.

## Slide 12
EDIT • test/test.py
8. Replace the example test with your test
SHIFT REGISTER QUICKSTART • Guide page 9
12
Test your shift register through its external pins.
01
Replace test/test.py with the supplied test.
02
Check reset, shift, hold, old data leaving and reset priority.
03
Compare each observed output with the expected value.
test/test.py — expected-value rule
# Shift the previous value and add the new bit.
expected = ((expected << 1) | bit) & 0xFF
assert await cycle(bit) == expected
CHECK
My test checks my circuit’s behaviour rather than the template’s example.
Notes: Guide page 9: 8. Replace the example test with your test
The template’s adder test cannot verify a shift register. Our Python test drives the wrapper’s pins and checks the output after clock edges.
In the extracted folder, open test/test.py. Use this complete file to replace the template’s test/test.py. cocotb is the Python tool that talks to the Verilog simulator.
Read the phases: reset, shift known bits, hold, shift more than eight bits so old data leaves, and reset while enable is 1. It also checks that unused outputs and bidirectional directions stay zero.
For your own design, change the expected result rule and input sequence to match its written behaviour. Keep checks at the external ports so the same test can run on the gate-level circuit.
Simulation = Running a model of the circuit before making hardware.
Assertion = A check that stops the test when the observed result differs from the expected one.
Pause and predict: After shifting 1 eight times from reset, what should the output be? What if enable then becomes 0?
Answer: 11111111. With enable = 0 it stays 11111111, even when serial_in changes.
Check: My test checks my circuit’s behaviour rather than the template’s example.
Full code (test/test.py — expected-value rule):
# Shift the previous value and add the new bit.
expected = ((expected << 1) | bit) & 0xFF
assert await cycle(bit) == expected

## Slide 13
EDIT • test/test.py / DETAIL
8. Replace the example test with your test
SHIFT REGISTER QUICKSTART • Guide page 9
13
PAUSE & PREDICT
After shifting 1 eight times from reset, what should the output be? What if enable then becomes 0?
Answer: 11111111. With enable = 0 it stays 11111111, even when serial_in changes.
CHECK
My test checks my circuit’s behaviour rather than the template’s example.
Notes: Guide page 9: 8. Replace the example test with your test
The template’s adder test cannot verify a shift register. Our Python test drives the wrapper’s pins and checks the output after clock edges.
In the extracted folder, open test/test.py. Use this complete file to replace the template’s test/test.py. cocotb is the Python tool that talks to the Verilog simulator.
Read the phases: reset, shift known bits, hold, shift more than eight bits so old data leaves, and reset while enable is 1. It also checks that unused outputs and bidirectional directions stay zero.
For your own design, change the expected result rule and input sequence to match its written behaviour. Keep checks at the external ports so the same test can run on the gate-level circuit.
Simulation = Running a model of the circuit before making hardware.
Assertion = A check that stops the test when the observed result differs from the expected one.
Pause and predict: After shifting 1 eight times from reset, what should the output be? What if enable then becomes 0?
Answer: 11111111. With enable = 0 it stays 11111111, even when serial_in changes.
Check: My test checks my circuit’s behaviour rather than the template’s example.
Full code (test/test.py — expected-value rule):
# Shift the previous value and add the new bit.
expected = ((expected << 1) | bit) & 0xFF
assert await cycle(bit) == expected

## Slide 14
BROWSER • CODE
9. Upload the complete seven-file adaptation
SHIFT REGISTER QUICKSTART • Guide page 10
14
Upload the contents of the extracted starter into your repository root.
01
Code → Add file → Upload files.
02
Drag info.yaml plus src, test and docs. Check all seven paths.
03
Commit to main: Add shift register. If needed, create and merge a pull request.
GitHub’s official Add file screenshot locates the upload control. Upload into your repository root.
CHECK
All seven files are saved at the intended paths, and the template infrastructure is still present.
Notes: Guide page 10: 9. Upload the complete seven-file adaptation
Extract shift-register-starter.zip. Open its contents until you see info.yaml beside src, test and docs.
In your own repository’s root, select Add file → Upload files. Drag info.yaml and the src, test and docs folders from INSIDE the extracted starter folder.
Check the paths: src/shift_register.v, src/project.v, test/Makefile, test/tb.v, test/test.py, docs/info.md and info.yaml. There must be no extra starter-folder prefix.
Enter Add shift register. For this personal practice repository choose Commit directly to main and save. A commit is a saved version. If GitHub requires a new branch, create a pull request and merge it into main. Check all seven files on main and note its commit identifier.
Folder dragging is unavailable → Open each existing file, select the pencil, replace its contents and commit. For src/shift_register.v use Add file → Create new file inside src. Check workflows only after all seven files are saved.
Check: All seven files are saved at the intended paths, and the template infrastructure is still present.

## Slide 15
BROWSER • ACTIONS → test
10. Check that your shift register passes
SHIFT REGISTER QUICKSTART • Guide page 11
15
Read the test result for the commit containing all seven files.
01
Actions → test → your final commit’s run.
02
Open the test job → Run tests. Zero failures or errors.
03
If it fails, fix the first error and save a new commit.
Official TEMPLATE Actions screen, for navigation only. Its red crosses are failed template runs, not your result. Your shift-register run has its own commit and result.
CHECK
The RTL test passed for my exact final commit, with zero failures and errors.
Notes: Guide page 11: 10. Check that your shift register passes
Each saved version can start checks. Open the run for the commit that contains your complete adaptation.
Select Actions → test → the run for your final commit. Confirm its branch and commit identifier.
Open the test job and expand Run tests. Read the final test summary: there must be no failures or errors. A green run from before your edit proves nothing about your new design.
If it fails, open the first assertion or compilation error. Fix that cause and save a new commit. The help sheet on page 13 covers common causes.
RTL test = A simulation of your Verilog source before it is converted into physical gates.
Pause and predict: What does a passing test establish?
Answer: The adapted circuit passed the cases and assertions you wrote. It does not prove every possible behaviour, timing corner or manufactured chip.
Check: The RTL test passed for my exact final commit, with zero failures and errors.

## Slide 16
BROWSER • ACTIONS → test / DETAIL
10. Check that your shift register passes — in practice
SHIFT REGISTER QUICKSTART • Guide page 11
16
PAUSE & PREDICT
What does a passing test establish?
Answer: The adapted circuit passed the cases and assertions you wrote. It does not prove every possible behaviour, timing corner or manufactured chip.
CHECK
The RTL test passed for my exact final commit, with zero failures and errors.
Notes: Guide page 11: 10. Check that your shift register passes
Each saved version can start checks. Open the run for the commit that contains your complete adaptation.
Select Actions → test → the run for your final commit. Confirm its branch and commit identifier.
Open the test job and expand Run tests. Read the final test summary: there must be no failures or errors. A green run from before your edit proves nothing about your new design.
If it fails, open the first assertion or compilation error. Fix that cause and save a new commit. The help sheet on page 13 covers common causes.
RTL test = A simulation of your Verilog source before it is converted into physical gates.
Pause and predict: What does a passing test establish?
Answer: The adapted circuit passed the cases and assertions you wrote. It does not prove every possible behaviour, timing corner or manufactured chip.
Check: The RTL test passed for my exact final commit, with zero failures and errors.

## Slide 17
BROWSER • ACTIONS → gds / docs
11. Build, check and look at the layout
SHIFT REGISTER QUICKSTART • Guide page 12
17
Verilog becomes physical gates and wires. Check every required job.
RTL test
docs
Separate workflows • same commit
GDS build
physical layout
Precheck + gate-level
rules + built behaviour
Viewer + artifacts
inspect + download
01
docs: download PDF/datasheet and check the pin table.
02
gds: check build, precheck, gate-level test and viewer.
CHECK
RTL, docs and every required gds job passed for one commit; I can open its layout and artifacts.
Notes: Guide page 12: 11. Build, check and look at the layout
The gds workflow turns Verilog into physical gates and wires. The docs workflow builds your datasheet. These run separately from the RTL test.
Open the docs workflow for the same commit. Confirm it succeeds. On its Summary page, scroll to Artifacts and download PDF; extract it and open datasheet.pdf. Check its pin table.
Open the gds workflow for that commit. Wait for the layout build, precheck, gate-level test and viewer jobs to complete successfully. Job labels can vary; open each job to see what ran.
Open the published Pages/viewer link from the run or repository Deployments. Zoom into the layout. On the gds run’s Summary page, scroll to Artifacts: download tt_submission (layout package) and GDS_logs (reports). Artifact names may change in later templates.
Artifact = A downloadable file produced by a workflow.
Gate-level = The circuit represented by the actual logic cells chosen during the build.
Check: RTL, docs and every required gds job passed for one commit; I can open its layout and artifacts.

## Slide 18
BROWSER • ACTIONS → gds / docs / DETAIL
11. Build, check and look at the layout — in practice
SHIFT REGISTER QUICKSTART • Guide page 12
18
Check | Plain meaning
Layout build | Place gates and connect them; inspect timing and geometry reports
Precheck | Check the design fits Tiny Tapeout’s integration rules
Gate-level test | Run your test against the generated gate connections
Viewer | Publish an image/browser view of the layout
Open the layout. Download tt_submission and GDS_logs.
CHECK
RTL, docs and every required gds job passed for one commit; I can open its layout and artifacts.
Notes: Guide page 12: 11. Build, check and look at the layout
The gds workflow turns Verilog into physical gates and wires. The docs workflow builds your datasheet. These run separately from the RTL test.
Open the docs workflow for the same commit. Confirm it succeeds. On its Summary page, scroll to Artifacts and download PDF; extract it and open datasheet.pdf. Check its pin table.
Open the gds workflow for that commit. Wait for the layout build, precheck, gate-level test and viewer jobs to complete successfully. Job labels can vary; open each job to see what ran.
Open the published Pages/viewer link from the run or repository Deployments. Zoom into the layout. On the gds run’s Summary page, scroll to Artifacts: download tt_submission (layout package) and GDS_logs (reports). Artifact names may change in later templates.
Artifact = A downloadable file produced by a workflow.
Gate-level = The circuit represented by the actual logic cells chosen during the build.
Check: RTL, docs and every required gds job passed for one commit; I can open its layout and artifacts.

## Slide 19
FINISH • CHECKLIST AND HELP
12. Keep your result and use the guide again
SHIFT REGISTER QUICKSTART • Guide page 13
Open reference ↗
19
Save one identifiable result: circuit, checks, layout and evidence.
01
Keep repository, commit and workflow links together.
02
Save the GDS, reports and datasheet for that same commit.
03
For your next design: map → wrap → list sources → test → build.
CHECK
I have saved a checked layout package for one identifiable commit.
Notes: Guide page 13: 12. Keep your result and use the guide again
You have finished this exercise when your adapted circuit is tested and its checked layout is archived. Fabrication is a separate later step.
Save the repository URL, commit identifier, test/gds/docs run links, downloaded GDS/reports and datasheet together. Match every item to the same commit.
Use the checklist: pin map agrees; three names agree; two source lists agree; tests pass; docs pass; all required gds jobs pass; layout and evidence are saved.
For another existing Verilog design, reuse this route: describe its behaviour, map its pins, wrap it, list its sources and write its tests. For an approved fabrication submission, choose the matching shuttle and follow the submission app’s current checks.
Unknown module / file not found → Page 7: check both source lists, filename case and the three top-module names.
Reset or shift assertion fails → Pages 5 and 9: check reset polarity, ui_in bit numbers, shift direction and expected values.
docs fails → Page 8: complete title/author/description and the three datasheet sections; preserve YAML indentation and pin keys.
Viewer fails but layout succeeds → Page 4: set Pages Source to GitHub Actions. Follow the linked FAQ’s rerun procedure.
Layout build or gate-level test fails → Open the first failing job’s log. Read synthesis/timing/geometry warnings. Correct the cause; unchanged reruns will not repair the design.
Check: I have saved a checked layout package for one identifiable commit.
Submission app — later, after approval: https://app.tinytapeout.com/
Official test guidance: https://tinytapeout.com/hdl/testing/
Workflow and viewer help: https://tinytapeout.com/faq/
Creating repositories from templates: https://docs.github.com/en/repositories/creating-and-managing-repositories/creating-a-repository-from-a-template
Uploading files: https://docs.github.com/en/repositories/working-with-files/managing-files/adding-a-file-to-a-repository

## Slide 20
FINISH • CHECKLIST AND HELP / DETAIL
12. Keep your result and use the guide again
SHIFT REGISTER QUICKSTART • Guide page 13
Open reference ↗
20
Unknown module / missing file
Check the three names and both source lists. Guide page 7.
Reset / shift assertion fails
Check pin bits, reset polarity and expected values. Pages 5 and 9.
Documentation fails
Complete metadata, sections and pin keys. Keep YAML indentation. Page 8.
Layout / viewer / gate test fails
Open the first failing job. Fix its cause; check Pages settings. Page 13.
CHECK
I have saved a checked layout package for one identifiable commit.
Notes: Guide page 13: 12. Keep your result and use the guide again
You have finished this exercise when your adapted circuit is tested and its checked layout is archived. Fabrication is a separate later step.
Save the repository URL, commit identifier, test/gds/docs run links, downloaded GDS/reports and datasheet together. Match every item to the same commit.
Use the checklist: pin map agrees; three names agree; two source lists agree; tests pass; docs pass; all required gds jobs pass; layout and evidence are saved.
For another existing Verilog design, reuse this route: describe its behaviour, map its pins, wrap it, list its sources and write its tests. For an approved fabrication submission, choose the matching shuttle and follow the submission app’s current checks.
Unknown module / file not found → Page 7: check both source lists, filename case and the three top-module names.
Reset or shift assertion fails → Pages 5 and 9: check reset polarity, ui_in bit numbers, shift direction and expected values.
docs fails → Page 8: complete title/author/description and the three datasheet sections; preserve YAML indentation and pin keys.
Viewer fails but layout succeeds → Page 4: set Pages Source to GitHub Actions. Follow the linked FAQ’s rerun procedure.
Layout build or gate-level test fails → Open the first failing job’s log. Read synthesis/timing/geometry warnings. Correct the cause; unchanged reruns will not repair the design.
Check: I have saved a checked layout package for one identifiable commit.
Submission app — later, after approval: https://app.tinytapeout.com/
Official test guidance: https://tinytapeout.com/hdl/testing/
Workflow and viewer help: https://tinytapeout.com/faq/
Creating repositories from templates: https://docs.github.com/en/repositories/creating-and-managing-repositories/creating-a-repository-from-a-template
Uploading files: https://docs.github.com/en/repositories/working-with-files/managing-files/adding-a-file-to-a-repository